## Slide 1: Security in Wireless Cellular systems (focus limited to authentication, at this stage)

## Slide 2: Architecture of wireless cellular systems (abstracted)
Uu
2/3G: MSC/VLR
4/5G: eNB/MME
2/3G: HLR/AuC
4G: HSS

## Slide 3: Security in 1G
Security?
Nah…!

## Slide 4: Security in 2G
Security? No problem!
Let me do it!!
Can you
Protect us?
COMP-128 Security by obscurity
No mutual auth (Rogue BS)
No core network security
. . . . . .

## Slide 5: Security in 3G
OK, let’s be serious now…
Pro to the rescue!!
(fairly) good ciphers - public scrutiny!
Multual authentication
Core network security
. . . . . .
Encryption AND (in part) Integrity
Multiple keys

## Slide 6: Security in 4G
Time for a Security architecture!
Systematic
approach

## Slide 7: Security in 4G and 5G
Security in 4G
(I) Network Access Security
(II) Network Domain Security
(II) Network Domain Security
(III) User Domain Security
(I) Network Access Security
(IV) Application Domain Security
(V) Service-Based Architecture Domain Security
(VI) Visibility and Configuration of Security
Time for a Security architecture!
Systematic
approach
Actually… this is already the 5G security architecture… to save one slide (couple of differences over 4G)!

## Slide 8: 5G Security Architecture - Components
DU Distributed Unit
CU Central Unit
N3IWF Non 3GPP Inter Working Function
AMF Access Management Function
SEAF SEcurity Anchor Function
SEPP Security Edge Protection Proxy
AUSF AUthentication Server Function
SIDF Subscription Identifier Deconcealment Fct
ARPF Auth credential Repository & Processing Fct
UDM Unified Data Management
UDR Unified Data Repository
There is IMHO NO such thing as a one-size trusted/untrusted 5G/6G network!
(my own technical explanation of why the geo-political security debate is in part ill-posed)
Improved key derivation  several different levels of trust (trust domains)
DU
CU
gNB
Serving network
non3GPP access
N3IWF
Home network
AMF
SEAF
S E P P
S E P P
AUSF
SIDF
ARPF
UDM
UDR
No security support in DU (deployed in untrusted sites)
Access Stratum Security terminated at CU
Manage Network Access Security (AMF+SEAF co-implemented)
Security for interconnection traffic
Implements UE authentication, stores key for later reuse
Deconceals User Identity (more later)
The 5G «vault» : User data (UDR) and credentials (ARPF) used by UDM authentication/identification functions
Security for non-3GPP access (Wi-Fi, etc)
L2 message integrity?
Improved AUTH and home control via Proof-of-Presence
Test Framework SCAS for Security Assurance

## Slide 9: But systems are way more complex
5G/6G
systems’ security:
A small part of a bigger picture!!
Mobile/IoT security
Applications
Hardware
Risk management
Implementation
Side channels
Interworking
Incremental deployment
Malware
… … …
… … …
… … …
… … …
… … …
… … …
… … …
Device manufacturing security
Firmware
No 5G security if
SW/HW implementation
is insecure!
Critical infrastructure = high tier threats
«They» might design vulnerabilities!
5G/6G security
SW networks, third party suppliers: Complexity, increased threat surface!
Too many «optional/should»
In the standard!
Very risky! (you might believe you are secured, while…)

## Slide 10: Challenge-Response authentication in Wireless Cellular systems

## Slide 11: Authentication: when (e.g. 2/3G)
MS
VLR
HLR
AUC
BSS/MSC
Loc. Upd. Request
IMSI, LAI
Update Loc. Area
IMSI, LAI
Auth. Param. Req.
IMSI
Auth. Info. Req.
IMSI
Auth. Info
(Auth. Parameters)
Auth. Info
(Auth. Parameters)
authentication
Activate ciphering
Update Location
IMSI, MSRN
Insert Subscrib. Data
IMSI, additional data
Insert Subscrib. Data
ACK
Locat. Upd. Accept
IMSI
Start Ciphering
Kc
Locat. Upd. Accept
Forward new TMSI
TMSI
TMSI Realloc Cmd
Locat. Upd. Accept
TMSI Realloc ACK
TMSI ACK

## Slide 12: Authentication in 2G (unilateral)
Authentication Request
Challenge: 128 bit RAND
A3
RAND
Ki
SRES
Authentication Response
Signed RESult: 32 bit SRES
Equal?
SRES
SN
MS
HN
IMSI, RAND
SRES, Kc
A8
RAND
Ki
Kc

## Slide 13: Triplets (Authentication Vector)
VLR
AuC
IMSI
<RAND, SRES, Kc> x N
Home operator
Serving operator
Idea: once in a VLR area, autentication will need to be performed MANY times
Hence deliver N triplets, to be used for N distinct authentications
IMPORTANT: VLR does NOT need to know authentication algo used (A3, A8)
  Triplet contains computed result by AuC
  A3, A8 run inside the SIM (given by operator)

## Slide 14: Authentication: details
A38 = A3 and A8 at same time
RAND
128 bit challenge
Ki
128 bit secret
SRES
32 bit
Kc
64 bits (well, 54 + ten 0s)
Deliberately weak?
Challenge response with:
  Challenge  RAND
  Secret  Ki
  Hash  A3 algorithm

## Slide 15: On the A3/A8 algorithms
Security by obscurity
  A3 algorithm CAN BE operator-specific!
  But most vendors originally used algo today called COMP128
  Non disclosed but…
    Reverse engineered? Leaked out?
COMP128 broken in 1998
    http://www.isaac.cs.berkeley.edu/isaac/gsm-faq.html
  Chosen challenge attack [1998, Briceno, Goldberg, Wagner]
    Ki disclosed through about 150.000 queries with suitably selected challenges  approx 8h in 1998
    Having Ki means cloning the card!
  Better attack [2002, Rao, Rohatgi, Scherzer, Tinguely]
    Less than 1 minute!
Lesson learned:
  Security by obscurity does NOT work!! Leave hash design to crypto experts

## Slide 16: Over the air attach
No mutual authentication!
Rogue BTS may easily perform the attach
  run it for sufficient time

## Slide 17: 3G/4G/5G authentication: AKA Authentication and Key Agreement (STRONGLY Simplified for our purposes; 3G terminology)

## Slide 18: Major differences with 2G
Mutual authentication!
  Optimized…
  Guaranteed freshness for auth parameters
More comprehensive security
  More keys and several extra details
    (we will not focus on this)
Algorithms FIRST scrutinized by research community, THEN selected
  The opposite of security by obscurity 

## Slide 19: Authentication Vector
VLR
MS
HLR /
AUC
IMSI
N x Auth Vector
Authentication Vector:
- XRES (expected result) as GSM SRES
- RAND as GSM RAND
- AUTN (Netw. Auth. token) - - -
- CK (cipher key) as GSM Kc
- IK (integrity key) - - -
RAND, AUTN
RES
RES
=
XRES?
Auth
Network!

## Slide 20: MS authentication
Usual challenge response, but different (public) algorithm
f2
RAND
K
RES
32-128 bit
f3
RAND
K
CK
Cipher key
128 bit
f4
RAND
K
IK
Integrity Key
128 bit

## Slide 21: Network Authentication
MS should send a nonce…
  1 extra message
Bright idea: use Sequence number as “implicit” nonce!
  Issue: MS and AuC must be (approx) synchronized
  And robust procedures for resync must be specified
HLR /
AUC
MS
SQN-MS
SQN-HE
VLR
SQN

## Slide 22: SEQ as nonce: idea
Current SQN-MS
stored
SQN
(included in AUTN)
(given by AuC)
Check
SQN = SQN-MS + 1
(or in appropriate
Tolerance range to cope with lost msg)
Use SQN as
“implicit” challenge!!
Once auth OK, update local SQN

## Slide 23: Network authentication: AUTN format
SQN
Sequence number
AMF
Auth & key mgmt field
MAC-A
Message Auth code
48 bit
16 bit: carries info on which algo or key to use if choice available,
sync window, etc (signalling info)
64 bit: allows MS to verify authenticity of Network!
f1
RAND
K
MAC-A
64 bit
AMF
SQN
MS: has all info needed to check that MAC-A transmitted by network is the same of MAC-A locally computed!
SQN guarantees defense against replay

## Slide 24: Minor detail: protecting SQN!
A privacy problem:
  By looking at SQN (stepwise increasing), eavesdropper may discriminate and track user!
Solution: mask SQN with Anonymity Key
SQN xor AK
Sequence number
AMF
Auth & key mgmt field
MAC-A
Message Auth code
f5
RAND
K
AK
Anonymity Key
48 bit